## Slide 1: ESRM 433 / SEFS 533 LAB 2
Intro to Coordinate Refence Systems (CRS)
Lidar Metadata
Introduction to LidR and RStudio
Accessing online help and documentations for LidR and RStudio

## Slide 2: How do we know where on Earth we are?
Use latitude and longitude?

## Slide 3: Is the Earth round?
No! – Well, kind of…
The Geoid Earth
This makes determining locations with coordinates difficult
We can approximate using an ellipsoid
Check out the field of geodesy https://en.wikipedia.org/wiki/Geodesy

## Slide 4: Coordinate Reference Systems (CRSs)
Geographic vs Projected
https://www.youtube.com/watch?v=xJyJlKbZFlc

## Slide 5: Geographic Coordinate System
Where to put your latitude and longitude lines or the model ellipsoid
Datum
  The reference point
  Most common in North America
  NAD27, NAD83, WGS 84

## Slide 6: Projected Coordinate System
How to draw a flat map in the location of the GCS

## Slide 8: Back to the DNR
Default: Washington State Plane South
Downloadable from DNR
  Digital Surface Model (DSM) Hillshade
  Digital Terrain Model (DTM) Hillshade
  DSM
  DTM
  Metadata
  Point Cloud

## Slide 9: Digital Surface Model Hillshade
First Returns
95th Percentile
A “Blanket”
Hillshade adds a light direction to give definition to the points

## Slide 10: Digital Terrain Model Hillshade
Ground Returns
Lowest lidar returns
Trees and buildings are removed
Hillshade adds a light direction to give definition to the points

## Slide 11: DTM vs DTM hillshade more on this next lab…

## Slide 12: Metadata
Produced by the acquisition company
Technical aspects
  Date
  Location and Area
  Lidar scanner used and point density
  Ground control
  Projection information
  More…

## Slide 13: RStudio and lidR
You are not expected to be fluent in R for this class
lidR is a package for R that is built to deal with lidar data
Basic R tutorial you can run trough to get more comfortable
  https://education.rstudio.com/learn/beginner/

## Slide 14: R code common issues
Forward Slash / vs Back Slash \
No spaces!
Quotation marks “”
Capitalization MaTtERs!
Ctrl + Enter to run a line of code
One wrong character will prevent your code from running!

## Slide 15: For the rest we will head to RStudio